## Slide 1
Digital Design & Computer Architecture (DDCA)
Slide 1 of 9
Design & Simulation of an Intelligent Traffic Signal System
Implementing Decision Logic using Pure Combinational Circuits
PROJECT TEAM MEMBERS
DEPARTMENT OF COMPUTER SCIENCE & ENGINEERING
1st Year / 1st Semester Academic Evaluation
2620030100
B. Revanth Kumar
2620030090
P. Rohan
2620080077
Jaya Haasika
2620030046
Eshha
2620030407
Chaitanya

## Slide 2
Digital Design & Computer Architecture (DDCA)
Slide 2 of 9
Urban Traffic Challenge
Conventional traffic signals rely on fixed-time delays regardless of real-time road occupancy. This creates unnecessary waiting times at empty roads and severe bottlenecks on heavily congested lanes.
An intelligent system dynamically evaluates vehicle presence using road sensors and provides real-time signal decision making.
Core Objective: "The system automatically adjusts signal decisions in real-time according to instantaneous traffic conditions using digital logic."
Fixed Timer Control
Ignores actual vehicle presence; causes high idle delay and wasted throughput.
Decision-Based Control
Uses combinational boolean logic to immediate trigger green signals for active lanes.
Introduction & Motivation

## Slide 3
Digital Design & Computer Architecture (DDCA)
Slide 3 of 9
Problem Statement
To design and simulate a fundamental digital traffic signal decision system that takes binary inputs from road vehicle sensors and yields optimized green/red output decisions through logic gates.
Focus: Demonstrating foundational 1st-year DDCA concepts using pure combinational logic design techniques.
1. Sensor Mapping
Represent traffic presence on intersecting roads using binary logic variables (A, B).
2. Logic Modeling
Construct truth tables mapping all possible traffic input combinations to signal outputs.
3. Boolean Expressions
Derive simplified algebraic equations ($G_A, G_B$) for optimal decision rules.
4. Gate Simulation
Implement and verify logic circuits using standardized simulation tools (e.g., Logisim).
Problem Statement & Objectives

## Slide 4
High-level block diagram showing signal processing flow from physical road detection inputs to final light indicators:
Digital Design & Computer Architecture (DDCA)
Slide 4 of 9
Traffic Sensors
Vehicle Detectors Road A (A), Road B (B)
Input Encoding
Clean binary conversion (0 = Clear, 1 = Traffic)
Decision Circuit
Combinational Logic (AND, NOT Gates)
Signal Outputs
Road A Green ($G_A$) Road B Green ($G_B$)
Combinational Design Note
The system operates entirely as a memoryless decision circuit. Outputs react instantly to input changes without internal state storage or feedback loops.
Practical Scope Boundary
Demonstrates the decision stage. Full deployment in real infrastructure requires secondary timer sequencing and interlocking relays for safety.
System Architecture

## Slide 5
Digital Design & Computer Architecture (DDCA)
Slide 5 of 9
Core Working Principle
A combinational logic circuit is a digital circuit whose output at any instant is determined solely by the current combination of inputs.
Sample Decision Rule
Road A receives a Green signal decision ($G_A=1$) if and only if traffic is detected on Road A ($A=1$) AND no traffic is detected on Road B ($B=0$).
Safety & Conflict Rules
Mutual Exclusion: Both intersecting roads must never receive a green signal simultaneously ($G_A \cdot G_B = 0$).
Default Safety Red: If both roads report vehicle traffic simultaneously ($A=1, B=1$), the basic decision model defaults signals to RED to prevent collision.
Emergency Priority ($E$): Can be integrated via OR-override gates to force green for priority vehicles.
Combinational Logic Design

## Slide 6
Digital Design & Computer Architecture (DDCA)
Slide 6 of 9
Truth Table for Two-Road Intersection Decision Logic ($A, B$ Inputs vs $G_A, G_B$ Outputs):
A (Road A) | B (Road B) | GA (Green A) | GB (Green B) | System Action / State
0 | 0 | 0 | 0 | No traffic (Both Red)
0 | 1 | 0 | 1 | Traffic on B (Green B)
1 | 0 | 1 | 0 | Traffic on A (Green A)
1 | 1 | 0 | 0 | Conflict (Safety Red)
Boolean Expressions
Insight:
Road A Signal Equation:
Road B Signal Equation:
Truth Table & Expressions

## Slide 7
Digital Design & Computer Architecture (DDCA)
Slide 7 of 9
Step 1: Input Toggle Binary Sensor Signals ($A, B$)
Step 2: Signal Inversion NOT Gates ($\neg A, \neg B$)
Step 3: Logic Decision 2-Input AND Gates
Step 4: Output Display Green / Red Light LEDs
Simulation Environment
The circuit design can be simulated and verified using standard schematic software:
INPUT A = 1
INPUT B = 0
GA = 1 (GREEN)
GB = 0 (RED)
Logisim / Logisim Evolution (Educational schematic tool)
Proteus PCB & VSM (Hardware simulation)
Digital by HNeemann (Fast digital logic simulator)
Circuit & Simulation

## Slide 8
Digital Design & Computer Architecture (DDCA)
Slide 8 of 9
Verification Matrix
Zero Processing Latency
Instant gate propagation response without software execution lag.
Low Implementation Cost
Requires minimal hardware components (Standard 74xx IC gates).
High Reliability
Immune to software crashes, operating system freezes, or memory leaks.
Educational Value
Ideal baseline model for understanding foundational digital logic concepts.
Test Case 2
A=1, B=0 → $G_A=1$
Test Case 3
A=0, B=1 → $G_B=1$
Results & Key Advantages

## Slide 9
Future Scope & Enhancements:
Digital Design & Computer Architecture (DDCA)
Slide 9 of 9
Thank You! Questions & Discussion Welcome.
Project Conclusion
This project successfully demonstrates how combinational logic design principles can be applied to build an intelligent, responsive traffic signal decision system. Binary Boolean expressions accurately model real-world road priorities and verify seamlessly in software simulation.
Conclusion & Future Scope